Disassembly of Spid Rotator motor.

First, before removing the cover with the stator magnets, mark how it is mounted.

If it is rotated 180 degrees when mounted, the rotation is reversed to the previous direction.

The cover cup is in a strong magnetic field!

To loosen AND put back the cover, use something (here a screwdriver) to prevent rotation of the shaft. This means that the rotor of the motor does not follow out.

It is now possible to pull out the rotor part, but be careful with the two carbon brushes.

How to remove the gliding bearing.

Use the hole in the bottom of the cover to gently knock out the Lock ring at the bottom with

for example a small clipped nail.

When re-mounting the cover put some grease on the end of the rotor shaft to secure the small washer in place.

73 and GL Rune/SM5CUI